## Slide 1: C2PU TELESCOPES
© C2PU, Observatoire de la Cote d’Azur,
Université de Nice Sophia-Antipolis
Jean-Pierre Rivet
CNRS, OCA,
Dept. Lagrange
jean-pierre.rivet@oca.eu
Version 02, 28/08/2016

## Slide 2: C2PU: two telescopes
West dome
Omicron telescope
East dome
Epsilon telescope
West (“Ouest” in French): omicron telescope (“omicron”: Greek leter for “O”)
East (“Est” in French): epsilon telescope (“epsilon”: Greek letter for “E”)
TWO 1-METER TELESCOPES

## Slide 3: C2PU: two telescopes
Omicron telescope
Epsilon telescope

## Slide 4: C2PU Telescopes : optical combinations
Cassegrain secondary focus
Primary mirror
(parabolic)
Secondary mirror
(hyperbolic)
F 13000 mm
D = 1040 mm
F / D = 12.5
Magnifies a lot
Narrow field of view
Best for planetary imaging
CCD camera
at secondary focus
AVAILABLE
ON BOTH
TELESCOPES !

## Slide 5: C2PU Telescopes : optical combinations
Pure primary focus configuration
Primary mirror
(parabolic)
CCD camera
at primary focus
F 2995 mm
D = 1040 mm
F / D = 2.88
Simple, perfect at center,
BUT strong coma
aberration off-axis !

## Slide 6: C2PU Telescope : optical combinations
Prime focus configuration with Wynne corrector
Primary mirror
(parabolic)
CCD camera
at corrected primary focus
F 3297 mm
D = 1040 mm
F / D = 3.17
Much better !
3-lens Wynne
coma corrector

## Slide 7: How focalization is done
Prime focus configuration with Wynne corrector
Focalization
All the focal assembly
(Wynne corrector + Camera)
can move up and down.
Fully motorized, computer-operated,
with position gauge
AVAILABLE
ON OMICRON
TELESCOPE ONLY !

## Slide 8: Sample image
Galaxy NGC 6946:
Distance:  10 Mly
App. size: 9.8  11 ‘
Telescope: omicron@C2PU
Focus: Primary + ParraCor
Camera: SBIG ST4000 XCM
Exposure: 90 x 2mn
Date: 14/09/2012
Author: David Vernet

## Slide 9: C2PU Telescopes : optical combinations
“Coudé” focus
Primary mirror
(parabolic)
Secondary mirror
(hyperbolic)
F = 36400 mm
D = 1040 mm
F / D = 35
Magnifies a lot
Very narrow field of view
Fixed focus
Best for “big” focal sensors
CCD camera
at coudé focus
AVAILABLE
ON EPSILON
TELESCOPE ONLY !
Optical bench
Celestial North pole
Polar axis
3rd mirror
(flat)
4th mirror
(flat)
5th mirror
(flat)

## Slide 10: Optical configurations
West dome
Omicron telescope
East dome
Epsilon telescope
Cassegrain focus
F/12.5 or F/9.0
(with focal reducer):
Spectroscopy,
Narrow field imaging.
Prime focus +
Wynne corrector
F/3.2:
Photometry,
Astrometry,
Occultations.
Wide field imaging.
Cassegrain focus
F/12.5 or F/9.0
(with focal reducer)
Spectroscopy,
Narrow field imaging.
Coudé focus F/35
Only for invited
instruments

## Slide 11: C2PU Telescopes : equatorial yoke mount
South pillar
North pillar
Yoke
Polar axis
Declination axis

H
Telescope’s tube
(Serrurier structure)
Yoke mount “pros and cons” :
Very stable mechanically
Low flexion
Limitations in accessible
sky zone (blind angles).
... More on that later.

## Slide 12: Omicron Telescope : accessible zone
Elevation:
h > 18°
Declination:
< 60°
Hour angle:
-6h < H < +6h

## Slide 13: Epsilon Telescope : accessible zone
Elevation:
h > 21°
Declination:
< 60°
Hour angle:
-5.3h < H < +5.3h

## Slide 14: ENJOY !